## Slide 1: REPORT FORMAT
Project Title: Fault Detection in Power Grid Using Machine Learning
Assignment Submitted by
Name: M B G Rama Krishna
Roll No.: 201918BT513
Course: BITS ZC425T
Work Integrated Learning Program
BIRLA Institute of technology and Science, Pilani

## Slide 2
Students Hall Ticket

## Slide 3
Abstract
This project explores the use of machine learning concepts, such as Artificial Neural Networks, for fault detection and location in a Power Microgrid.
In microgrids, electronic equipment requires secure protection against short circuit faults to prevent de-energization of the entire system, which can have a significantly negative impact.
Transient circuit faults occur when conductors come in contact with each other or ground, with ground faults being the primary concern and accounting for over 80% of all faults.
This project presents a highly effective approach that uses an Artificial Neural Network (ANN) to detect and locate faults before they impact other system parts, thereby providing more dependable microgrid protection.
This project centers on the detection and location of faults on electric power transmission lines within the power microgrid network.

## Slide 4: Objectives
The objectives of the project are as follows:
Detecting faults and identifying the location of the faults on electric power transmission lines in the power microgrid network.
To protect the microgrid system using an Artificial Neural Network (ANN) that will detect and find the location of the fault before it affects other parts of the system.
Implement a machine learning model to identify the fault in Power grids.

## Slide 5: Types of Faults In a MicroGrid
There are broadly two types of faults that occur in a microgrid
Line-to-Line Fault
Line to Ground Fault.
Most of these faults are line-to-ground faults due to component or segment failure or lightning. When a short circuit fault happens in the microgrid, the fault resistance tends to zero and the current tends to become infinite.
I f →∞, R f →0
Here I f is the fault current and R f is the fault resistance.

## Slide 6: Key Idea for Detection of Faults
The breakers are initially at state 1 i.e., not activated. Now they are activated one by one for half an hour each time to get the dataset. Each breaker is activated at every hour of the day. So, in total, we get a total of 96 data points.
At every point secondary current (I sec) and load power value are taken into consideration along with their time of activation. The time of fault plays a significant role because of the nature of the circuit.
When the fault is introduced in the circuit a sudden surge of current is seen and a dip in the load power. When the battery controller is working the base of the surge is zero but when the battery controller is switched off the base of the surge power is different.

## Slide 7: Input Data Generation
We measure the values of secondary current (I sec), Load power (PL) consumed by the loads, and the time at which this data is measured for a period of 24 hours measuring after every 60 minutes.
In this way, we get 23 sets of values of all these parameters. We train this dataset (link below) in our ANN model.
Now using this trained dataset, the location can be known as the fault before the first house or the second house, and so on.
Here the model consists of three houses, so the dataset obtained is not noticeably big, but a large dataset can be obtained by including more loads i.e., houses.

## Slide 8: ANN Model
The ANN model consisted of an input layer of dimension 92X27, two hidden layers and a final output layer consisting of 4 neurons (softmax layer).
The input consists of 4 features that are listed:
1. The current in the circuit.
2. The load power.
3. The time at which the breaker was switched on.
4. The result.
Since the “Time” feature contains only 24 values and is of classification type, so we encode it (one hot encoding) thus making the overall input features equal to 27.

## Slide 9: Conclusion
A small-scale modelling of the microgrid including solar panels, battery energy storage system, loads and AC grid is simulated in MATLAB. A sudden change in the value of secondary current I sec and the load power P L is the basis for the algorithm that detects the fault location.
Here we observe the spikes in the graph of I sec as the faults. These faults are generated manually by switching on each of the circuit breakers at various moments of a day.
Also, the faults were studied by keeping as well as isolating the battery controller. Having generated the data at various times of a day and training the dataset in ANN fetched a decent accuracy of (70%~80 %). So having new data of power, I sec and time of the day, we can predict if there is a fault or not, and if there is, the location of the fault can be determined accurately.